## Slide 1: Estimation of brain microstructural parameters with diffusion MRI
Abrar Faiyaz
Department of Electrical and Computer Engineering

## Slide 2
Figure 1: Schematic depiction of differences between low-IQ and high-IQ individuals with regard to brain volume, neurite density and orientation dispersio. (Genç, E 2018, Nature Communications)
Neurites are the structural units of the brain. Histological analysis of neurite physiology has helped us understand
  Brain development1 (Conel, 1939)
  Brian Aging2 (Jacobs et al., 1997)
  Functional behavior3 (Jacobs et al., 2001)
  Pathological changes4 (Fiala et al ., 2002)
Magnetic resonance imaging is non-invasive and can quantify changes in mm scale with T1w, T2w, FLAIR, diffusion MRI.
Example in the right shows how neurite orientation and density can differentiate low and high IQ individuals. (Genç, E 2018, Nature Communications)
Possible MR tools for microstructural abnormality investigation-
Diffusion weighted MRI
fMRI- BOLD,
MRE etc
Introduction
Advanced mathematical model to get these microstructural parameters works with certain dMRI protocols that pose constraint on clinical MR scans.
Notes: Might look like an MR scan will replace GRE in the future 🤖 … ?
Intellectual performance is likely to benefit from this kind of microstructural architecture since restricting synaptic connections to an efficient minimum facilitates the differentiation of signals from noise while saving network and energy resources
# Conel looked at the

## Slide 3
Diffusion in MR: Quantified as the amount of signal loss when diffusion sensitized gradient is applied.
Commonly used sequence for dMRI. Diffusion sensitizing gradient field G introduced for time twice in spin echo sequence.
B
D
b-vector (g) encoding on unit sphere: (C) cART (D) CSVD
C
Diffusion MRI
Sequence in figure B is repeated with different gradient directions g, to solve for diffusion tensor D
Ref
Net spin in a spin echo sequence
A
S0
Notes: 1. In diffusion MRI, the term diffusion is based on the physics that when a gradient is applied the regions of hindered diffusion will result in higher signal and there will be signal loss at the regions of free diffusion.
2. The first figure with blue dots give a representation of water molecules in a restricted region moving with brownian motion.
3. Now we represent the net spin (or the magnetic alignment of that region) in figure A. Here in figure A. we see a common spin echo sequence where Echo is the read MR signal after applying 90* and 180* pulse. The read signal is the signal that we get from the restricted region. So, we can say the spin echo sequence is the common way we quantify signal of a voxel.
Now, the only thing that's left is adding the diffusion gradient to this sequence.
4. At figure B, We apply two same diffusion encoding gradient before and after the 180* pulse and the Gradient applied are of opposite polarity. So, effect of opposite gradients cancel out for a "spin that doesn’t move" and signal over there is higher. Opposite happens for the spins that moves.
Also the higher the number of repetation in different direction, the better diffusion analysis. And the minimum has to be 6 acquisions to be able to solve this (5) equation s=s0exp(-bgDg). B-value is defined with this equation and is directly proportional to the gradient strength and time delay. Gamma is the gyromagnetic ratio.
6. On these unit spheres, b-vector or directions of the gradients is shown for cART and CSVD study. This is the small g in the equation. Lastly, a slice for different diffusion direction is shown for ongoing CSVD study
###Any free system with a constant gyromagnetic ratio, such as a rigid system of charges, a nucleus, or an electron, when placed in an external magnetic field B (measured in teslas) that is not aligned with its magnetic moment, will precess at a frequency f (measured in hertz), that is proportional to the external field:, f = (gyromag ratio/ 2pi) * B

## Slide 4
Step 1: Solve for the components of D. (weighted least square method)
Step 2: Find 3 largest eigenvalues for D i.e. and
Diffusion Tensor Imaging (DTI) (Koay, C. G. et al 2006)
Normalized variance of largest 3 eigenvalues (Fractional Anisotropy),
Mean Diffusivity
Radial Diffusivity
Axial Diffusivity
Step 3: Calculate FA, MD, RD, AD.
Diameter of axon+ myelin ~0.0005mm
# of axon in white matter
~4000 in (2x2x2mm)
,
Notes: In diffusion MRI, the first step is to calculate the components of D, and to do that we need to solve the objective function you are seeing in step 1, where yi is log of S0 and W_ij is constructed based on the power component of the exponential. And gamma_j is the components of D arranged in such a way that the first equation is satisfied.
After identifying the gamma that is all the D components, we calculate the highest eigenvalue-eigenvector pairs and use the eigenvalues to calculate FA,MD,RD and AD.

## Slide 5
DTI SCALARs | FA (normalized variance of the eigenvalues) | MD (λ1+λ2+λ3)/3 | AD λ1 | RD (λ2+λ3)/2
 | FA is a summary measure of microstructural integrity. While FA is highly sensitive to microstructural changes, it is less specific to the type of change. | MD is an inverse measure of the membrane density, is very similar for both GM and WM and higher for CSF. MD is sensitive to cellularity, edema, and necrosis. | AD tends to be variable in WM changes and pathology. In axonal injury AD decreases. The ADs of WM tracts have been reported to increase with brain maturation. | RD increases in WM with de- or dys-myelination. Changes in the axonal diameters or density may also influence RD.
Gray Matter | ↓ | − | ↓ | ↑
White Matter | ↑ | − | ↑ | ↓
CSF | ↓ | ↑ | ↑ | ↑
High myelination | ↑ | ↓ | − | ↓
Dense axonal packing | ↑ | ↓ | − | ↓
WM Maturation | ↑ | ↓ | ↑ | ↓
Axonal degeneration | ↓ | ↑ | ↓ | ↑
Demyelination | ↓ | ↑ | − | ↑
Low SNR | ↓ | ↑ | ↓ | −
DTI scalars in pathological cases
Notes: These dti scalars are directly related with changing brain macrostructural integrity. We see from different studies, how change in different dti scalars have been related with high myelination, dense axonal packing, WM maturation, Axonal degradation, demylination. Previous literatures report this on Alzheimers, Parkinsons etc neurocognitive diseases.
Table:
https://thewinnower.com/papers/3524-dti-scalars-fa-md-ad-rd-how-do-they-relate-to-brain-structure

## Slide 6
Figure 1. Left part of diagram shows that standard imaging methods provide one value (gray level) for every 3D position p. That value or gray level may code for the linear x-ray attenuation coefficient at CT or for the relative signal intensity at MR imaging. Right part of diagram shows that in diffusion imaging every 3D position p (voxel) is associated not with a gray level but with a 3D image that encodes the molecular displacement distribution in that voxel. The value measured at the coordinates p,r—ƒ(p,r)—indicates the proportion of molecules in the voxel that have moved the given distance r.
DTI : Limitations(Hagman, P. et al, 2006)
Ellipsoid model with the eigenvalues cannot distinguish
- crossing fiber and isotropic configuration (a,c)
- standing water compartments.
- complex fiber orientations.
- intra/extracellular differentiations.
Possible configuration and their simulated displacement
Notes: The DTI ellipsoid model with the eigenvalues cannot distinguish crossing fiber voxel with actual isotropic voxels. Here all the 4 images shown are simulations of displacement profile using some fiber orientation and specific diffusion tensor. In the simulation a and c it is clear that one is crossing fiber and another is stationary water probably CSF in the brain. But when we reconstruct our tensors with 3 eigenvalues that’s not possible to understand in general diffusion model. Secondly, complex fiber orientations cannot be captured with this model and the intracellular and extracellular information cannot be distinguished by this model.
https://doi.org/10.1148/rg.26si065510

## Slide 7: Hypothesis behind DTI and NODDI
Figure: Image under Transmission electron microscopy
Diameter of axon+ myelin ~0.5 µm
Around ~4000 in (2x2x2mm) voxel
Myelin water
Extracellular water
Intracellular water
DTI
NODDI
(a)
(b)
(c)
(d)
(e)
Notes: In this slide you'll understand the distinction between DTI and NODDI. Before I jump to that, let’s see a microscopic environment inside the brain in figure e. This is a typical image that can be seen under transmission electron microscope. You can see three different compartments that holds H+ ions here. Extracellular, intracellular and myelin water, the signal can also be free water inside the same voxel. Although myelin water is not relevant here, you can see that we can separate out the myelin water signal at lower TE but intracellular and extracellular signal remains combined when TE is around 100ms (figure B).
In summary,
When we get a signal from a voxel of 2mm resolution, that signal has contributions from isotropic, extracellular water and intracellular water. Generally diameter of an axon is around 0.5 micrometer, So in one voxel there’s a lot of configuration possibility of fibers and free water.
So, let’s see what DTI does to understand these configurations. Per voxel, a diffusion tensor is assumed which is solved. And this tensor is represented with their highest 3 eigenvalues. That visualizes the diffusion on an ellipsoid formed with those eigenvalues.
But NODDI changes the physics of the problem. We consider each signal to be a combination of 3 compartment with different diffusion coefficient. Parallel, hindered and isotropic diffusion per voxel. To account for what is the amount of contribution, a probability term volume fraction is given to each generated signal from individual compartment.
##########
In figure A we see T2 decay curve and figure B shows T2 distribution from white matter. So it actually depends on the selection of the echo time to separate myelin water signal and intra-extra cellular signal. When Echo time is around 100ms, we can see that the intracellular and extracellular signals are merged. Here’s where NODDI model comes in and setup a probabilistic model that can solve for intracellular and extracellular water contribution.
(A) T2 decay curve and (B) T2 distribution from human white matter. Inset in (B) shows a cross-section through an axon with the locations of intra/extracellular water and myelin water.
So, what we see here signal contribution for intracellular and extracellular cases is merged.
Images:
https://www.slideserve.com/kaylee/schwann-cells
https://www.britannica.com/science/myelin
Laule, C., Vavasour, I.M., Kolind, S.H. et al. Magnetic resonance imaging of myelin. Neurotherapeutics 4, 460–484 (2007). https://doi.org/10.1016/j.nurt.2007.05.004

## Slide 8
The diffusion ellipsoids and tensors for isotropic unrestricted diffusion, isotropic restricted diffusion, and anisotropic restricted diffusion are shown.
P. Mukherjee et al. AJNR Am J Neuroradiol 2008;29:632-641
©2008 by American Society of Neuroradiology
DTI
NODDI
Complex configurations
Simple representation
of complex configurations
Notes: So, we already saw there can be many possible tissue configurations in a single voxel. And you can actually quantify them based on the set of components in the D matrix.
Simply said, NODDI is capable of explaining more complex configurations along with the simple ones. Where DTI represents simple or complex configuration in simple ellipsoids.
###
What I mean is that, # show images
The diffusion ellipsoids and tensors for isotropic unrestricted diffusion, isotropic restricted diffusion, and anisotropic restricted diffusion are shown.
Diffusiion trajectory incase of free water, when random barriers present and when axonal bundles are coherent are shown here.

## Slide 9
In simpler terms,
  Intra-Cellular Volume fraction (ICVF or vic)
    – represents fiber/axon density.
    – also termed as Neurite Density Index (NDI).
    – Signal contribution of fibrous compartment.
  Orientation Dispersion Index (ODI) – denotes the geometry of the fibers.
  Isotropic Volume fraction (ISO) – denotes the standing water content in the voxel
Notes: Here, I have shown examples of the DTI scalar and NODDI microstructure maps.

## Slide 10: Background: NODDI (Zhang,2011,2012)
Figure 1. Illustration of a set of Watson distributions with the same mean orientation but different orientation dispersion index: OD ∈ {0.04, 0.16, 0.5, 0.84, 1.0}.
Where, q and b are the gradient direction and b-value of diffusion-weighting, respectively;
f(n)dn gives the probability of finding sticks along orientation n; gives the signal attenuation due to unhindered diffusion along a stick with intrinsic diffusivity d∥ and orientation n.
NODDI parameters to fit
V_ic: intra-cellular volume fraction.
κ: concentration parameter of Watson distribution
μ: mean orientation of Watson distribution ().
V_iso: isotropic volume fraction
()
Maximum Likelihood estimation for fitting parameters,
(Rician log-likelihood function for measured (M) and generated signal (A))
Extracellular signal model
Standing water signal model
Intracellular signal model
2 slides here . Explain what icvf… terms mean
Notes: NODDI model calculates signal A and tries to fit it with measured signal M with maximum likelihood framework with rician loglikelihood function.
I’ll explain how this model generates signals when a protocol is given [a protocol is a set of b-value denoted by b and bvectors denoted by q here].
To characterize the brain tissue, NODDI assumes there are 3 signal contributions.
The simplest signal model comes from the standing water signal and as modelled with the exponential decay with a known diffusion coefficient from the literature.
The second one is the Intracellular signal model. This is the cdf of the probability density function modelled with a confluent hypergeometric function called Watson distribution (illustrated at right). It has a kappa parameter that determines the geometry of the fiber. The cdf is weighted with exponential decay with a constant diffusion coefficient factor for each sampled direction.
The third one is the extracellular signal model and whose diffusion coefficient is related to parallel diffusion coefficient. And the cdf is calculated with the help of an analytical form.
This 3 signals are then weighted with a probabilistic contribution from each compartment termed as volume fraction.
### Possible questions-
Why exponential decay? Because any signal whether it be from extracellular, intracellular or isotropic, with increasing b-value it will decay exponentially. That’s how MR signal from any substance decays
###
Add more slide regarding how they said 1 shelled estimation is not good.

## Slide 11: NODDI fitting alternatives ( to address fitting time and multi-shell constraint)
AMICO (Daducci et al., 2015)
q-space DL(Golkov et al., 2016)
MEDN, MEDN+(Ye 2017)
MESC-Net(Ye 2019)
DLpN(Faiyaz 2022)
(a)
(b)

## Slide 12
Thanks!